## Slide 1
Kermit Wies
CMAP
September, 2011

## Slide 2
micro
Meso
Macro
CMAP’s Mesoscale Freight Model predicts how freight moves into, through and out from the region.
The middle section of our 3-tiered Freight construct

## Slide 3: Why did we develop the Mesoscale Freight Model?
Our current model estimates only trucks based on observed counts
the economic choices made for goods movement across multiple modes and commodities
GO TO 2040 requires a freight modeling tool that explains

## Slide 4: How does the Mesoscale Freight Model work?
Firm Generation
Supplier Selection
Flow Apportionment
Path Selection
Industry
Manufacture Leather Products
1-10
10-100
Location
Harvey
Maywood
>100
Aurora
Wauconda
Size
For each Firm
Commodities Transported
Select Suppliers
Top 5 Supply Industries
Shippers
Receivers
Commodities
Receivers
Path
Mode
Logistics
Distance
Size
Commodities
Shippers
Products
Receivers
Total annual logistics costs (G) (by commodity type) =
order costs (O)
+ transport and intermediate handling costs (T)
+ deterioration and damage costs (D)
+ capital costs of goods during transit (pipeline costs Y)
+ inventory costs (I)
+ capital costs of inventory (K)
+ stockout costs (Z)

## Slide 5: What data does the Mesoscale Freight Model need?
Commodity Flows
Make and Use Tables
County Business Patterns
Regional Employment Data
Rail, Highway, Air and Marine Networks

## Slide 6: What does the Mesoscale Freight Model do?
Tracks individual firms and transactions
Commodity Flows
Logistics Details
40,000 Suppliers
691,000 Buyers
2,100,000 Shipper-Receiver Pairs
Live animals/fish
Cereal grains
Other ag prods.
Animal feed
Meat/seafood
Milled grain prods.
Other foodstuffs
Alcoholic beverages
Tobacco prods.
Building stone
Natural sands
Gravel
Nonmetallic minerals
Metallic ores
Coal
Crude petroleum
Gasoline
Fuel oils
Coal-n.e.c.
Basic chemicals
Pharmaceuticals
Fertilizers
Chemical prods.
Plastics/rubber
Logs
Wood prods.
Newsprint/paper
Paper articles
Printed prods.
Textiles/leather
Nonmetal min. prods.
43 Commodities
55 Logistics Alternatives

## Slide 7: What does the MesoScale Freight Model tell us?
The effects of different scenarios.
For example:
Logistics Park Calumet
How?
Add a logistics node at the LPC location
Activate a short line RR between nearby railyards and water ports
Model
The
Run

## Slide 8: FY12 Freight Modeling Priorities
Evaluate Freight Scenarios
  GO TO 2040 Policies: Truck pricing, Brownfield redevelopment (COD), CREATE
  Freight System: Combined Infrastructure Recommendations (CS).
Freight MacroModel Development
  Permits MesoModel to be used in forecasting
Data development for MesoModel
  Permits MesoModel to be calibrated and validated
  Goal: incorporate into CMAP production models
Staff
Consultant
Staff and Consultant